## Slide 1: Pulsed Power Supplies
For Plasma Nitriding Process
MAGPULS GmbH

## Slide 2: MAGPULS QT-1000/600/1500 bp QuickSwap
Pulsed power supply for Plasma Nitriding with vacuum chamber size of:
L x D = 15 m x 5 m
Technical data:
DC Power : 0 – 600kW DC Pulse current: up to 1500A peak DC current: 0 – 600A DC Pulse Voltage: 50 -1000V Puse On time: 5µs – 1000 µs Pulse Pause time: 5µs - 1000 µs Pulse frequency: DC/ 500 Hz – 16 kHz Duty Cycle: 0,1 % up to 99,5 % Cooling: Water cooling and air condition Ambient Temp.: 10°C up to 45° C Mechanical data: Pulse unit: Cabinet HxBxT = 2200x1200x800mm DC power sypply: Cabinet HxBxT = 2200x1200x800mm
Construction: Pulse unit is built up in 19“ rack mount units mounted in a cabinet with copper rail systems at the rear side for easy service and inspection.
DC power supply in thyristor controlled technology
MAGPULS GmbH

## Slide 3: MAGPULS QT-1000/600/1500 up QuickSwap
Pulse power cbinet
DC power cbinet
MAGPULS GmbH

## Slide 4: Internal construction of the MAGPULS QT 1000/600/1500 bp
Control unit
Pulse booster
300A DC / 750A peak current
Place for upgrade of higher pulse power
MAGPULS GmbH

## Slide 5: MAGPULS 800/160/1000 up QuickSwap
Technical data:
DC Power : up to 160kW DC Pulse current: up to 1000A peak Pulse Voltage: 50 -800V Puse On time: 5µs – 100sec. Pulse Pause time: 5µs - 100 sec. Pulse frequency: DC/ 0.5 Hz – 16 kHz Duty Cycle: 0,01 % up to 99,9 % Cooling: Water cooling Ambient Temp.: 10°C up to 40° C Mechanical data: Cabinet HxBxT : 2200x1200x800mm
Construction: Pulse unit is built up in 19“ rack mount units mounted in a cabinet with copper rail systems at the rear side for easy service and inspection.
Inclusive switch over device for oparating with 2 vacuum oven at the same time while one oven is cooling down.
MAGPULS GmbH

## Slide 6: MAGPULS QT-800/450/500 up
Technical data:
DC Power : 0 – 360kW DC Pulse current: up to 500A peak DC current: 0 – 450A DC Pulse Voltage: 50 -800V Puse On time: 5µs – 1000 µs Pulse Pause time: 5µs - 1000 µs Pulse frequency: DC/ 500 Hz – 16 kHz Duty Cycle: 0,1 % up to 99,5 % Cooling: Water and air cooling Ambient Temp.: 10°C up to 40° C Mechanical data: Pulse unit: Cabinet HxBxT = 2200x600x800mm DC power sypply: Cabinet HxBxT = 2200x1200x800mm
Construction: Pulse unit is built up in 19“ rack mount units mounted in a cabinet with copper rail systems at the rear side for easy service and inspection.
Commissioning at the customer‘s site
MAGPULS GmbH

## Slide 7: MAGPULS QT-800/50/200 up
Technical data:
DC Power : 0 – 40kW DC Pulse current: up to 200A peak DC current: 0 – 50A DC Pulse Voltage: 50 -800V Puse On time: 5µs – 1000 µs Pulse Pause time: 5µs - 1000 µs Pulse frequency: DC/ 500 Hz – 16 kHz Duty Cycle: 0,1 % up to 99,5 % Cooling: Water and air cooling Ambient Temp.: 10°C up to 40° C Mechanical data: Cabinet HxBxT: 2100x1200x800mm
Construction: Pulse unit is built up in 19“ rack mount units mounted in a cabinet.
DC power supply in thyristor controlled technology
MAGPULS GmbH

## Slide 8: MAGPULS 800/420/1000 up
Technical data:
DC Power : 0 – 340kW DC Pulse current: up to 1000A peak DC current: 0 – 420A DC Pulse Voltage: 50 -800V Puse On time: 5µs – 1000 µs Pulse Pause time: 5µs - 1000 µs Pulse frequency: DC/ 500 Hz – 16 kHz Duty Cycle: 0,1 % up to 99,5 % Cooling: Water and air cooling Ambient Temp.: 10°C up to 40° C Mechanical data: Pulse unit: Cabinet HxBxT = 2200x600x800mm DC power sypply: Cabinet HxBxT = 2200x1200x800mm
Construction: Pulse unit is built up in 19“ rack mount units mounted in a cabinet with copper rail systems at the rear side for easy service and inspection.
DC power supply in thyristor controlled technology
System in operation at customer‘s site
MAGPULS GmbH

## Slide 9: MAGPULS QP-800/400 up
Technical data:
DC Power : 0 – 40kW DC Pulse current: up to 400A peak DC current: 0 – 80A DC Pulse Voltage: 50 -800V Puse On time: 2µs – 100 sec Pulse Pause time: 2µs - 100 sec. Pulse frequency: DC/ 500 Hz – 20 kHz Duty Cycle: 0,01 % up to 99,9 % Cooling: Water and air cooling Ambient Temp.: 10°C up to 40° C Mechanical data: Pulse unit: 19“ x 6HU x 650mm DC power supply: 2 x ( ½ 19“ x 4HU x 600mm)
Pulse unit and DC power supplies mounted in a cabinet
MAGPULS GmbH

## Slide 10: Connecting at the rear side
MAGPULS GmbH